## Slide 1: Can We Make Physics-Informed AI Actually Solve Physics Efficiently?
From beam-vibration reproducibility to a compute-aware Physics Reference Layer
Physical system
Physics equations
PINN
Verified physical reference
AI application
the missing piece we are researching
First testbed: Euler–Bernoulli beam vibration
[Author name] · [Institution] · October 2026
Notes: NOTICE: the pipeline. Physics-based AI needs a trustworthy physical reference between the equations and the application. That reference is what we are researching. MEANING: our first testbed is a vibrating beam. It is simple enough to have an exact solution, so every claim can be checked, and hard enough (fast, long-lasting vibration) to expose PINN failures. NEXT: why this matters, and why we looked at physics-informed neural networks at all.

## Slide 2: Engineering needs fast, trustworthy physics
WHY THIS PROBLEM MATTERS
computational cost per answer →
physical trust →
Physics simulation
accurate, verifiable — expensive per query
Pure ML
fast — but can violate physics
TARGET
accurate + cheap + verified
PINN
physics inside a neural network
?
The research question
HIGH PHYSICAL ACCURACY
+
LOW COMPUTATIONAL COST
+
PHYSICAL VERIFICATION
PINNs promise all three at once. Do they deliver on a real vibration problem?
Notes: NOTICE: the map. Classical simulation is trustworthy but costs a full solve per answer. Pure machine learning is fast but has no guarantee of obeying physics. A PINN puts the governing equations into the network's training objective, so in principle it can be both. The orange box is where we want to be. MEANING: the question is not 'can a network fit a curve'. It is whether we can get accuracy, low cost and verification together. The literature is honest about cost: PINNs are typically much slower to train than classical solvers but fast to evaluate once trained (Grossmann et al., 2024). NEXT: the published method we started from.

## Slide 3: A 2025 paper: a PINN for beam vibration
WHERE WE STARTED
1 Beam
Chart: 
2 Physics equation
EI·u_xxxx + ρA·u_tt + b·u_t = 0
bending stiffness · inertia · damping
3 PINN
A neural network u(x, t), trained until it satisfies the equation, the initial shape and the clamped ends
Our test case: clamped–clamped, damped beam, first mode at 20.6 Hz, i.e. 20.6 vibration cycles in the 1-second window.
PUBLISHED BASELINE
Söyleyici & Ünver, Engineering Applications of Artificial Intelligence 141 (2025) 109804
Fourier features + NTK adaptive weighting
The paper's contribution: a PINN for beam vibration covering high-frequency cases, several boundary conditions and experimental validation.
4.64 × 10⁻⁴
relative L2 error reported by the paper for our test case
Published value — not our result.
Notes: NOTICE: the chain beam → equation → PINN. The network takes position and time and outputs displacement; training penalises any violation of the beam equation, the initial shape and the clamped ends. MEANING: the reference paper (Söyleyici & Ünver, EAAI 2025) adds two published techniques: Fourier features, which help networks represent fast oscillations, and NTK-based adaptive weighting of the loss terms. It reports a relative L2 error of 4.64e-4 for our test case. That is the paper's number, not ours, and Fourier + NTK is the paper's method, not our contribution. Our test case: clamped–clamped damped beam, first mode, 20.6 Hz, so the model must reproduce about 20.6 decaying cycles in one second. NEXT: what we actually did with it.

## Slide 4: An experiment ladder: one question per step
WHAT WE ACTUALLY DID
0
Published Fourier + NTK
The paper's method — our starting point
1
Baseline reproduction
Does a faithful implementation reproduce it?
2
D · Configuration diagnostics
Which implementation choices matter?
3
E · Hard constraints + RAD
Can hard constraints remove the failure?
4
X · Conditioning + representation
Is representation the problem?
5
Y · Optimizer
Is optimization the problem?
6
Z · Sampling / seed / batch
Can sampling or batch size fix propagation?
7
Budget study · Y1-20K, Z4-20K
Does more physics computation extend persistence?
26
controlled training runs
one change at a time
Kept identical across runs: the beam, the exact reference solution, the evaluation grid, the seed (one controlled exception) and the compute accounting.
Notes: NOTICE: read the ladder top to bottom; each rung asks one question and changes one thing relative to the rung before. MEANING: first we checked whether a faithful implementation of the paper reproduces its behaviour. When it did not, we did not pile on tricks; we isolated causes: implementation choices (D), hard constraints and adaptive sampling (E), conditioning versus representation (X), the optimizer (Y), sampling, seed and batch size (Z), and finally how much physics computation the solver gets (the 20 000-step budget runs). 26 runs in total, single seed 1234 except one seed-change control (Z2). NEXT: what these runs actually produced — the clearest single picture of Batch 1.

## Slide 5: From a static field to eight cycles — then collapse
WHAT HAPPENED
How close does each stage get to the real vibration? (mid-span displacement u(L/2, t), mm)
exact solution
collapse (amplitude < 50 % of exact)
C0
paper method: Fourier + NTK · 20k steps
Chart: 
Static collapse
never vibrates · L2 3.26
X2
hard constraints + tanh²(ω₁t) · 5k steps
Chart: 
Conditioning improved
vibrates, but over-damped · L2 0.909
Z4
+ LR schedule, batch 128 · 5k steps
Chart: 
collapse | -100 | 100
≈ 3.2 cycles
longer persistence · L2 0.526
Z4-20K
same recipe, 4× compute · 20k steps
Chart: time t [s]
collapse | -100 | 100
≈ 8.1 cycles
then still collapses · L2 0.263
Notes: NOTICE: grey is the exact beam response — 20.6 decaying cycles. Each coloured line is one stage of our investigation, same time axis. C0 (red), the paper's Fourier + NTK method implemented faithfully: it never vibrates; it sits near a static deflection (relative L2 3.26 after 20 000 steps). X2 (amber): with exact hard constraints and a better-conditioned time factor it starts from the right shape and vibrates, but dies out far too fast (L2 0.909). Z4 (teal): with a decaying learning rate and larger batches it follows the first ~3.2 cycles (L2 0.526). Z4-20K (orange): the same recipe with four times the physics computation follows ~8.1 cycles, then still collapses at 0.393 s (L2 0.263). MEANING: every step moved the failure later. None reproduced the full window. All four curves are inference from frozen checkpoints; the collapse times shown equal the frozen Batch-1 values exactly. NEXT: why each of these failures happened.

## Slide 6: Three different failures, found one at a time
WHY DID IT FAIL?
A
SOFT TRAINING FAILURE
Does the published setup vibrate?
B
CONDITIONING FAILURE
How large must the network output be?
C
LONG-TIME PROPAGATION FAILURE
Where in time is the vibration lost?
Chart: t [s]
Fourier + NTK → static / incorrect attractor
The published baseline did not reproduce sustained vibration in our controlled implementation.
Chart: t [s]
(t/T)² → required |N| ≈ 8.4 × 10³
tanh²(ω₁t) → required |N| = O(1)
Hard constraints fixed IC/BC satisfaction, but the original time factor was poorly conditioned.
Chart: t [s]
collapse | -100 | 100
correct first cycles
amplitude decay
collapse
More compute moves collapse later, but does not remove it.
Notes: NOTICE: three panels, three different failure mechanisms, each found by a controlled experiment. A — the paper's soft-constraint training (initial and boundary conditions as penalties, NTK weights). In our implementation it settled into a static, non-vibrating solution while the NTK weights grew to roughly 1e14–1e15. We call this an observed optimization failure; we do not claim the NTK weights cause it. B — we then built the initial and boundary conditions into the network exactly ('hard constraints'). The original time factor (t/T)² forces the network to output about 8,369 in magnitude near t = 0 — a badly conditioned target. Replacing it with tanh²(ω₁t), where ω₁ comes from the beam equation, brings the required output to order one (at most 1.9). The chart is the required network output computed from the exact solution. C — with conditioning fixed, the model learns the first cycles correctly, then the amplitude decays too fast and the vibration collapses. More physics computation moves this collapse later but has not removed it. NEXT: what these experiments let us conclude.

## Slide 7: Claim → evidence
WHAT WE LEARNED
1
Representation is not the main limit
Trained directly on the exact solution (no physics loss), the same network recovers 129.25 and 129.37 rad/s (X3, X4); exact 129.32 rad/s.
2
Conditioning matters
(t/T)² hard constraint needs |N| ≈ 8.4 × 10³; tanh²(ω₁t) needs O(1). Only the tanh² variants started to vibrate.
3
Compute matters
Persistence 1.2 → 3.1 → 3.2 → 8.1 cycles (Y1 5k → Y1 20k → Z4 5k → Z4 20k; 0.16M → 2.56M PDE evaluations).
4
RAD did not solve the failure
Z1 (Y1 + residual-adaptive sampling): 1.6 cycles, then collapse — no long-time oscillation.
5 STATUS: NO VALIDATED OPTIMIZED PINN YET
Best tested (Z4-20K): 8.1 of 20.6 cycles, L2 0.263, still over-damped. Full-window reproduction was not achieved.
Notes: NOTICE: each claim on the left is tied to one measured piece of evidence on the right. 1 — Representation: when we trained the same network directly on the exact solution (a diagnostic, not a solver), it reproduced the 20.6 Hz vibration. So network capacity is not what blocks us. 2 — Conditioning: how the constraints are built into the network changes the required output by more than three orders of magnitude, and only the well-conditioned version vibrated. 3 — Compute: persistence grew from 1.2 to 8.1 cycles as physics computation grew. 4 — Adaptive sampling (RAD) did not fix the collapse. 5 — and the honest status: no optimized PINN has been validated. The best tested model reproduces 8.1 of 20.6 cycles. NEXT: the compute story in one graph.

## Slide 8: More physics computation helps — but not enough yet
THE COMPUTE STORY
Chart: Does additional physics computation delay dynamic collapse?
| 0.16 | 0.32 | 0.48 | 0.64 | 0.64 | 1.28 | 1.92 | 2.56 | 0 | 3
Y1 recipe, batch 32 (5k–20k steps) | 1.1732 | 1.6775 | 2.1355 | 3.108
Z4 recipe, batch 128 (5k–20k steps) | 3.1543 | 5.1199 | 7.1216 | 8.0941
Full-window target (20.6 cycles) | 20.6 | 20.6
≈ 20.6
FULL-WINDOW TARGET (cycles)
≈ 8.1
BEST TESTED (cycles)
Z4-20K, the best tested model
2.56M PDE evaluations · L2 0.263
≈ 8.1 cycles · collapse at 0.393 s
frequency ≈ 129.2 rad/s (exact 129.32)
Not the same budget as the paper. The paper reports L2 ≈ 4.64 × 10⁻⁴ after its full schedule (≈ 2.88 × 10⁷ PDE evaluations by our reading of it); our best tested is L2 0.263 at 2.56 × 10⁶.
Clearly helps; the full-window threshold has not been crossed.
Notes: NOTICE: horizontal axis is how many times the physics equation was evaluated during training; vertical axis is how many vibration cycles the model reproduces before it collapses. The grey line at the top is the target: all 20.6 cycles. MEANING: along both recipes, more physics computation monotonically delays the collapse — from 1.2 cycles at 0.16 million evaluations to 8.1 cycles at 2.56 million. At equal computation (0.64 million) the small-batch and large-batch recipes land in the same place (3.1 vs 3.2 cycles), so batch size mainly changed wall-clock time, not the solution. The last block of computation gained about half as much as the previous blocks, so we do not extrapolate. The paper's 4.64e-4 comes from its full training schedule, roughly ten times more PDE evaluations than our largest run, so the numbers are not a like-for-like comparison. Our controlled implementation did not reproduce the published result; the investigation identified implementation, conditioning and optimization sensitivities. NEXT: what this means for how we continue — Batch 2.

## Slide 9: Batch 2: From PINN Optimization to a General Physics Solver
WHAT WE ARE DOING NOW
PHYSICAL PROBLEM
PHYSICS ANALYSIS
CONDITIONING
FORMULATION
REPRESENTATION
TRAINING STRATEGY
PHYSICS SOLVER
VERIFICATION
PHYSICS REFERENCE
NOT
one PINN recipe for every PDE
BUT
choose a solving strategy based on the physics and the compute budget
“We are not trying to make PINNs more complicated. We are trying to make physics solving more efficient and adaptive.”
Building blocks already in the literature — we benchmark them, we do not claim them: mixed formulations · modal PINNs · temporal decomposition · hard constraints and tanh²-type conditioning · adaptive sampling · loss balancing · optimizers · automated PINN design.
RESEARCH HYPOTHESIS — UNDER INVESTIGATION
Problem-dependent, compute-aware selection of the solving strategy, with built-in verification. Not an established contribution.
Status: preparation done; first controlled Batch-2 diagnostics started (single seed, provisional — not presented as evidence).
Notes: NOTICE: the left column is the pipeline Batch 2 studies. The middle stages — conditioning, formulation, representation, training strategy — are exactly where Batch 1 found the solver to be sensitive. MEANING: Batch 1 showed there is no single setting that 'fixes' the PINN; what helped depended on the physics (conditioning) and on the compute budget. So Batch 2 asks a broader question: can the solving strategy be chosen from measurable properties of the problem and the available compute, with every answer verified against physics before it is returned? Honesty about novelty: mixed formulations, modal PINNs, temporal decomposition, hard constraints and tanh²-type conditioning, adaptive sampling, loss balancing, optimizers and automated PINN design all have prior art (Batch-2 literature matrix, 81 works). We benchmark them. The candidate gap — problem-dependent, compute-aware strategy selection with verification — is a research hypothesis under investigation, not a result. Status: Batch-2 preparation and pre-registration are done and the first controlled diagnostics have started; they are single-seed and provisional and are not presented as evidence today. NEXT: where this leads.

## Slide 10: From railway to vertical AI
WHERE THIS LEADS
We did not simply add components to a PINN. Controlled experiments located where the solver fails: the network can represent the dynamics; conditioning and optimization limit it; physics-computation budget measurably matters. Next: a problem-aware, compute-aware Physics Reference Layer — not another fixed PINN recipe.
RAILWAY
STRUCTURAL
THERMAL
FLUID
ENERGY
MANUFACTURING
PHYSICS REFERENCE LAYER
CURRENT
beam physics research
NEXT
general solver research
FUTURE
railway Physics Reference Layer
LATER
other vertical AI applications
RAILWAY PATH · future work — no railway results exist yet
Beam vibration
Rail dynamics
Vehicle / track dynamics
Axle / bearing dynamics
Sensor-informed physics
Predictive maintenance
Notes: FINAL MESSAGE: We did not simply add more components to a PINN. We used controlled experiments to determine where the solver fails. We found that the network can represent the target dynamics, identified conditioning and optimization limitations, and measured the effect of physics-computation budget. That motivates the next phase: a problem-aware, compute-aware Physics Reference Layer rather than another fixed PINN recipe. NOTICE: the Physics Reference Layer sits between physics and application AI. Railway is the first application we will target; structural, thermal, fluid, energy and manufacturing are later candidates. The timeline on the right is the honest status: today we are doing beam physics research; next is general solver research; a railway Physics Reference Layer is future work; other verticals come later. The railway path along the bottom is a plan, not a result. Only the first box — beam vibration — has been studied, and even there no validated optimized PINN exists yet. No railway model has been trained.

## Slide 11: Technical setup: PDE and PINN architecture
APPENDIX A · BACKUP
Physics (benchmark FE-D-M1) | 
Equation (paper Eq. 49) | c²·u_xxxx + u_tt + γ·u_t = 0 (EI·u_xxxx + ρA·u_tt + b·u_t = 0 divided by ρA)
Coefficients | c² = 43.73², γ = 7.08
Domain | x ∈ [0, 2.75] m, t ∈ [0, 1] s
Boundary conditions | clamped–clamped: u = u_x = 0 at both ends
Initial conditions | u(x,0) = Mode-1 shape, A₀ = 0.08 m; u_t(x,0) = 0
Mode 1 | ω_d = 129.32 rad/s (20.6 Hz); decay 3.54 s⁻¹
References | paper-faithful (printed root 4.7300) and exact-physics (exact root); they differ by 4.386e-4 relative L2
Evaluation | 201 × 2001 grid; relative L2; persistence = first t ≥ P/2 where local amplitude < 50 % of exact
PINN (published baseline and our variants) | 
Network | 6 × 200 tanh, 241,601 parameters
Fourier features | spatio-temporal multiscale, m = 100; σ_x = 1; σ_t = 10, 1
Paper training | NTK trace weights; Adam lr 1e-4; 640 points per term, mini-batch 32; 45,000 epochs
Hard constraints | u = u₀(x) + g(t)·Φ(x)·A₀·N(x,t), Φ = 16x²(L−x)²/L⁴
Time factor | g = (t/T)² (original) or tanh²(ω₁t), ω₁ = 129.37 rad/s from the PDE and BCs
LR schedule (Y, Z) | 1e-3 · 0.9^(step/1000)
Hardware | CPU, 1 thread per run, float32, seed 1234
Budgets | 5,000–20,000 steps; 1.6e5–2.56e6 PDE evaluations
Notes: Backup only. Exact definitions behind the main talk. Sources: references/batch1/reports/STAGE0_AUDIT.md, STAGE01_CORRECTIONS.md, CONVENTIONS.md, PHASE_X_DIAGNOSTIC.md, PHASE_Y1_20K_BUDGET_DIAGNOSTIC.md.

## Slide 12: Detailed experiment matrix (26 runs, frozen)
APPENDIX B · BACKUP
Run | Change vs parent (5k steps unless noted) | L2 | Outcome
BA | plain MLP (20k) | 2.60 | no oscillation
BB | + Fourier features (20k) | 1.81 | static / low-freq.
C0 | paper: Fourier + NTK (20k) | 3.26 | static
C0-rc | C0, reference-code convention (20k) | 1.73 | static
D1 | C0 + unit-normalised inputs | 1.78 | static
D2 | C0 + zero biases | 2.49 | low-freq., wrong ω
D3 | C0 + unit inputs + zero biases | 1.86 | low-freq.
D4 | C0, ref.-code conv. + zero biases | 1.11 | low-freq.
E3 | BB + RAD | 2.21 | offset, no oscillation
E4 | hard constraints, (t/T)² | 2.83 | slow decay, no oscillation
E5 | E4 + RAD | 2.84 | no oscillation
E4b | E4, ref.-code convention | 1.61 | no oscillation
X1 | E4 with tanh²(ω₁t) | 1.50 | static / low-freq.
Run | Change vs parent (5k steps unless noted) | L2 | Outcome
X2 | E4b with tanh²(ω₁t) | 0.909 | 112 rad/s, over-damped
X3 | supervised fit (diagnostic) | 0.463 | 129.25 rad/s
X4 | supervised fit (diagnostic) | 0.316 | 129.37 rad/s
Y1 | X2 + LR schedule | 0.774 | 1.2 cycles, collapse
Y2 | X1 + LR schedule | 1.47 | static / low-freq.
Y3 | X4 + LR schedule (diagnostic) | 0.120 | 129.32 rad/s
Y4 | C0 + LR schedule | 2.75 | static
Z1 | Y1 + RAD | 0.718 | 1.6 cycles, collapse
Z2 | Y1, seed 1235 | 0.799 | 1.1 cycles, collapse
Z3 | Y4 + RAD | 2.60 | static
Z4 | Y1, mini-batch 128 | 0.526 | 3.2 cycles, collapse
Y1-20K | Y1, 20k steps | 0.550 | 3.1 cycles, collapse
Z4-20K | Z4, 20k steps | 0.263 | 8.1 cycles, collapse
L2 = relative L2 error vs the exact solution (= paper-faithful reference at this precision). Italic rows are supervised diagnostics, not physics-trained solvers. Persistence in cycles uses the frozen collapse metric.
Notes: Backup only. L2 values are read at build time from references/batch1/optimization_leaderboard.csv (frozen, byte-identical to ROOT). Outcomes from the Phase A1, D, E, X, Y, Z and budget reports.

## Slide 13: Literature frontier: what already exists
APPENDIX C · BACKUP
Mixed / auxiliary formulations
Lyu et al. 2022 (MIM); A-PINN for EB beams 2026
Modal / reduced-order PINNs
Zhang, Vlachas & Chatzi 2026 (RO-PINN)
Temporal decomposition
Krishnapriyan et al. 2021; Penwarden et al. 2023; AT-PINN-HC (Chen et al. 2025)
Hard constraints, tanh²-type conditioning
Sukumar & Srivastava 2022; Lu et al. 2021 (hPINN); AT-PINN-HC auxiliary functions 2025
Adaptive sampling
RAR (Lu et al. 2021); RAD (Wu et al. 2023); R3 (Daw et al. 2023)
Loss balancing
Wang et al. 2021 (LR annealing); NTK (Wang et al. 2022); ReLoBRaLo; SA-PINN 2023
Optimizers and precision
Adam + L-BFGS / NNCG (Rathore et al. 2024); MultiAdam 2023; SOAP 2025; FP64 (Xu et al. 2025)
Representation
Fourier features (Tancik 2020; Wang 2021); SIREN 2020; SPINN 2023
Automated PINN design
Auto-PINN 2022; PINNsAgent 2025; Lang-PINN 2025
Our status: every component above has prior art — benchmarked, not claimed.
Candidate gap (RESEARCH HYPOTHESIS): selecting the strategy from measurable physics properties before training, under a compute budget, with verification — closest prior work selects by search or LLM agents (Auto-PINN, PINNsAgent, Lang-PINN).
Notes: Backup only. From the Batch-2 literature audit (PINN-RP docs/LITERATURE_MATRIX.md and docs/NOVELTY_GAP.md): 81 works tabulated, 65 confirmed by web search, the rest from bibliographic memory and flagged. Abstract-level reading; full texts must be checked before any publication claim.